## Slide 1: Updated minuets OBD on UDS
From 4-9-20 meeting
Notes from Marl Laleman – Ford
Vehicle E E System Diagnostic Standards Committee Chair

## Slide 2: IUMPR alternate proposal status
-Alternate proposal details are still under review by industry, Alliance meeting on April 14th to continue discussion
-In previous discussion, CARB request parameter to show a history of the value prior to reset by running diagnostic
-A. Zettel presented some details of new parameter for EWMA values, presentation will be provided once industry consensus is reached

## Slide 3: NRC/Timeout for message too long
-In cases where a message may be too long to fit into that maximum CAN message size, NRC 0x14 will be sent to the tool in response
-Specific case discussed is when “DTCs not Complete” requested right after powerup, or after code clear, and module supports more than 1000 DTCs
-J1979-2 will document the NRC requirement, and any timeout parameter needed to be implemented by the tools
-J1978 will also need to address how NRC is handled, team will ensure discussion occurs
  Additional 100 msec P2 timing information
    -See attached from Eric Swenson

## Slide 4: CARB request for Streaming Data
-CARB requested a streaming data function similar to J1939 functionality, with DID request made once, and repetitive response without additional tool request
-Service $2A/$2C functionality exists in ISO 14229, however requires additional service tool content, and would be difficult to standardize
-CARB asked if existing internal CAN network communication could be monitored by tool, e.g. module to module communication of Engine RPM as an example
-On vehicles that support J1979, the internal communication is not standardized, even between electrical architectures within an OEM, and there are security concerns with monitoring this traffic.
-CARB/J1979-2 committee agreed to discuss this as a potential future update, not as part of this regulatory update

## Slide 5: Freeze Frame Priority request
-CARB proposed that a phase-out of Misfire/Fuel Freeze Frame priority could be accommodated
-Some OEMs would like to retain priority to avoid changing their diagnostic manager handling of similar conditions
-Other OEMs would like to retain priority to ensure technicians see frames for Fuel/Misfire codes, as these benefit from freeze frame analysis
-Debate over whether 5 frames would be enough to ensure technician gets adequate data, more frames can be optionally supported if OEM is concerned
-Point from G. Potter, why is phase-out necessary if CARB will allow priority initially in UDS? CARB indicates priority handling issues are common mistakes
-CARB to internally discuss how to address priority, provide feedback.

## Slide 6: Readiness per OBD ECUs that support CCM
-CARB question regarding how tool would determine correct readiness status for vehicle CCM
-PID $01 is required for all modules that support CCM today, expected that the new equivalent would also be required on all modules that support CCM.
-PID $00 has a bit that indicates to the tool if PID $01 is supported. The GST would be required to indicate which modules had reported readiness, and the status of that module.
-The GST should also be able to indicate it did not get an expected response. J1699 would check this also.
-J1979-2 will document the required “ping” message for the tool to determine what OBD modules are present

## Slide 7: Walk Ins Substitute for J1699 testing on Early Vehicles
-Concern that J1699 updates will not be ready for 22/23MY vehicles
-How will vehicles be validated?
-CARB intends to include regulatory language that will require manufacturers to use alternate methods to prove compliance, similar to when J1699-3 was being developed.